## Slide 1: 11676 Midterm Project
Predict ocean health, one plankton at a time
Hailun Zhu

## Slide 2: Project Purpose
Problem statement
  Plankton are critically important to our ecosystem. Loss of plankton populations could result in ecological upheaval as well as negative societal impacts, particularly in indigenous cultures and the developing world.
  Traditional methods are time consuming and cannot scale to the granularity or scope necessary for large-scale studies
  Predict ocean health, one plankton at a time.
Value proposition if solution found
  New way for measuring and monitoring plankton populations.

## Slide 3: Analytic Approach
Feature extraction
  Rescale image
    25 X 25
    50 X 50
  Max Region Properties feature(interested object)
    Ratio
    filled_area: Number of pixels of filled region
    Perimeter: Perimeter of object which approximates the contour as a line through the centers of border pixels using a 4-connectivity.
    solidity : Ratio of pixels in the region to pixels of the convex hull image.
  SIFT feature

## Slide 4: Analytic Approach
Feature extraction
  SIFT feature
    Scale-invariant feature transform (or SIFT)
    Rotation-invariant
    Key points count
  Mahotas feature
    Local binary patterns (LBP) – texture extraction
    Zernike moments - shape descriptors

## Slide 5: Analytic Approach
Classifier test
  Decision tree number: 100 / 200
Final approach utilized to generate the best results
  Feature vector:
    rescale_image(50X50), ratio, filled_area, perimeter, solidity, sift_count, sift
  Decision tree number: 200

## Slide 6: Results
Summary of performance
  Feature extraction
feature | Accuracy of cross validation | Accuracy of the test | Running time
rescale_image(25) | 0.451280580405 | 0.460853799242 | 856.844261885
rescale_image(50) | 0.461760744425 | 0.469589582999 | 1080.51703596
ratio | 0.469759054329 | 0.467776495797 | 1097.83636689
ratio + properties | 0.480298560882 | 0.481457062799 | 1060.66653109
SIFT | 0.497728131152 | 0.501895500247 | 1118.52025390
SIFT + count | 0.505686500742 | 0.508653370694 | 1150.40613484
LBP | 0.497933914394 | 0.503543761332 | 1279.74228287
Zernike moments | 0.500700147492 | 0.501521674633 | 1350.40613484

## Slide 7: Results
Summary of performance
  Classifier test
  Best:
    N = 200
feature | Accuracy of cross validation | Accuracy of the test | Running time
N = 100 | 0.505686500742 | 0.508653370694 | 1150.40613484
N = 200 | 0.506615930376 | 0.512114718971 | 1750.24850917

## Slide 8: Error Analysis
The features do not include all the information. Most of the features only provide the shape information of the image and only consider the rotation of the image.
For example, I do not use feature to compute holes and sharp curves in the image, which might be an important characteristic of the image.

## Slide 9: Error Analysis
Some of the shapes are difficult to distinguish.
1. Images in same class looks not the same
acantharia_protist
3721.jpg vs 3733.jpg

## Slide 10: Error Analysis
Some of the shapes are difficult to distinguish.
2.Images in different class look similar
acantharia_protist 337.jpg
acantharia_protist_big_center 29759.jpg

## Slide 11: Actionable Information or Insights
Extract feature focus on target object region instead of the whole image.
Use image feature extraction algorithm that is rotation-invariant.
Use better classifier

## Slide 12: Future Work
Adding features that could provide information that focus on edge cases like curves and holes, so that features could cover more cases.
Using a more state-of-art classifier, or test with other classifier like SVM.

## Slide 13: Supplemental Information
Python lib used:
  skimage
  sklearn
  opencv
  mahatos